## Slide 1
III Digital Audio
III.1 (Fr Sept 30) Audio Encoding

## Slide 2
content
neutral niveau
aesthesis
communication
semiotics
poiesis
expression
physical reality
signification
General Scheme of Audio Encoding
analog digital

## Slide 3
analog digital encoding
voltage
analog
mixer
analog
mixer
analog
mixer
digital
mics
voltage
analog
loudspeakers

## Slide 4
microphone types
moving coil dynamic
ribbon = thin corrugated metal
condenser = dynamic capacitor
Lorentz force on electrical charges

## Slide 5
microphone polar patterns
omnidirectional bidirectional cardioid hypercardioid

## Slide 6
loudspeaker anatomy
tweeter (high)
midrange
(sub)woofer (low)
Cone vibrates
Outer supension (surround)
Inner supension (spider)
Dust cap
Coil
Permanent magnet
Cone
Electrical signals

## Slide 7
encoding of sound
mechanical: LP
magnetic: Analog Tape
magnetic: DAT = Digital Audio Tape
HD = Hard Drive
optical: CD = Compact Disk
electric: (semiconductor-based)
volatile, e.g. RAM (Random Access Memory)
semi-volatile, e.g. Memory Sticks
non-volatile, e.g. ROM (Read Only Memory)
analog
digital
0100001010100100010001010

## Slide 8
mechanical: LP
magnetic: Analog Tape
analog
1877 Thomas Alva Edison’s phonograph vertical print on tin foil
1888 Emil Berliner’s horizontal printing
1931 RCA vinyl (PVC) 331/3 RPM, 30 cm ∅
1935 AEG, BASF/3M (!!)
9.5 cm/sec, amplitude ~ magnetization ← The Tascam 85 16B analog tape recorder 16 tracks of audio on 1 inch (2.54 cm) tape.
VHS analog video by JVC 1976
Alan Blumlein 1930

## Slide 9
digital
0100001010100100010001010
optical: CD = Compact Disk
Commercial since 1982 by Philips & Sony
Herbert von Karajan recorded Richard Strauss’s Alpensinfonie 120 mm diameter, 80 min audio ~ 700 MB
By 2007 200 ×109 CDs sold!
laser reading 0001110110100111001010000111110000111.....
Polycarbonate
track width ~1μm
land
pit

## Slide 10
1Bit 0 or 1
4 Bit 0000, 0001, ... 1111 = 16 values 0,1,2,3....15
CD has 16 Bit amplitude quantization:
16 entries: 101.....1 = 1  215 + 0  214 + 1  213 + ...1  20
0,1,..., 65‘535 = 216 values
1. amplitude quantization
binary representation of numbers:
1011 means (sign!!)
1  23 + 0  22 + 1  21 + 1  20 = 8 + 2 + 1 = 11
CD has 44‘100 samples per second
CD of one hour and stereo has total of
2 channels  60 minutes  60 seconds  44‘100 samples  16 amplitude Bits = 635 MByte (1 Byte = 8 Bits)
2. time quantization
?

## Slide 11
digital
0100001010100100010001010
electric: (semiconductor-based)
volatile, e.g. RAM (Random Access Memory)
semi-volatile, e.g. Memory Sticks
non-volatile, e.g. ROM (Read Only Memory)
magnetic:
HD = Hard Drive, non-volatile
Invented 1956 by IBM
5000 RPM
“Ring” writing element
longitudinal recording (standard)
air cushion 10 nm
hair = 50 μm
magnetic: DAT = Digital Audio Tape1983
99 kHz sample rate & 24 Bit resolution